## Slide 1
1 mm thick CdTe + Timepix3 ASIC
SINGLE-LAYER COMPTON CAMERA (slcc)
Lojius Lombigit1, Dima Maneuski2 & Benedikt Bergmann3
1Technical Support Division, Malaysian Nuclear Agency, 43000, Kajang, Selangor
2SUPA School of Physics and Astronomy, University of Glasgow, Glasgow, G12 8QQ, United Kingdom
3Institute of Experimental and Applied Physics, CTU in Prague

## Slide 2
Introduction
1
Kinematic of single-layer Compton camera
2
Proof of concept
3
Result
4
Conclusion
5
Contents

## Slide 3
Compton camera is a novel gamma camera concept that relies on the Compton kinematic for image reconstruction
What is Compton camera?
Single-layer Compton camera (SLCC) is a single detector system where recoiled electron and scattered photon are detected on the same detector volume.

## Slide 4
Hybrid Pixel detector based on Timepix3 readout ASIC
Event Count + iToT
2015: 130 nm CMOS
Pixels: 256 x 256
pitch: 55 m
ToT + ToA
ToA only
Semiconductor detectors
(Si, GaAs, CdTe, CZT)
Energy resolution:
< 600e- (FWHM)
ToA: 1.562 ns
Min. detectable Charge: > 500e-
Frame-based or
Data-driven
**ToT = Time over Threshold (Energy measurement)
** ToA = Time of Arrival (Time measurement)

## Slide 5
KINEMATICS of slcc

## Slide 6
KINEMATICS of slcc
Valid event
Valid event
Invalid

## Slide 7
Selection of valid Compton events
Events that correspond to energy deposition of recoiled electron & scattered photon
Finding the z-axis coordinate
Pixel detectors only registered x & y pixel coordinates.
Scattering Angle
Challenges
Filtering the XRF (Cd & Te)
XRF = byproduct of photoelectric.
Introduced error during image reconstruction
Depth difference: Computed from time different between two events
Two events that occurred within the pre-defined clustering time.
Total energy =[E_ ± ]
Energy cuts:
E_recoiled  [EXRF ±  ]
3D pixel separation
Event due to recoiled electrons must be on the top.
Scattering Angle that
Produced conic surface

## Slide 8
D. Turecek et. Al., (JINST 2020) demonstrates SLCC on 2 mm thick CdTe with 131I (364 keV), 22Na (511 keV) & 137Cs (662 keV)
Tc-99m (140 keV) on thinner CdTe sensor?
Proof of concept
Z48
E  140 keV

## Slide 9
Institute of Experimental & Applied Physics (IAEP) , CTU of Prague.
Detectors: 1 mm thick, 55 m-pitch, 256 x 256 CdTe sensors + Timepix3 readout ASIC, Vbias = - 300 V.
Photon source: 1 MBq, 57Co (122 keV).
Acq. time: 3600 s & 1800 s (data-driven ToT + ToA mode).
DAQ : Katherine readout & Burdamann software.
Experiment setup
Hybrid pixel detectors (CdTe + Timepix3)
50 mm
ZL 60 mm
57Co

## Slide 10
Data analysis
Clustering:
Full-length charge collection time (FLCC)  32 ns
Two Coincidence Events:
Energy cuts:
Python 3 IDE
(Numpy, SciPy, Matplotlib, LMFIT)
Assigning
Compute
&
Select
Image reconstruction

## Slide 11
Result
Coincidence < 0.2 %
Cone reconst. Data < 8 %

## Slide 12
Result

## Slide 13
Limited valid Compton events
Photoelectric absorption is dominant (@ 122 keV)
Detector thickness
XRF event suppression
Energy cut is insufficient
Selection by 3D pixel distance
Technology works
Timepix3 superior ToA resolution @ 1.562 ns
Simultaneous Energy (ToT) & Time (ToA) measurement
Compton event selection algorithm proven

## Slide 17
> 90
Hyperbola surface